ILC250 parameter sets -
Comparison GuineaPig - CAIN
ILC250 machine was discussed in more detail at AWLC2017 at SLAC
Different parameter sets are under discussion to increase the luminosity
CAIN simulation was done by Daniel Jeans to look at the luminosity, and the pair background envelopes
See talks by Kaoru Yokaya and Daniel Jeans
https://agenda.linearcollider.org/event/7507/contributions/39290/attachments/31821/47993/HigherLumi250GeV-AWLC2017-Yokoya.pdf
https://agenda.linearcollider.org/event/7507/contributions/39291/attachments/31828/48012/mdi-beamparams-awlc-2017.pdf

---
ILC250 parameter sets
From talk by Yokoya
Set 1: TDR
Set 4: TDR + ex

---
ILC250 parameter sets
Variations of the new ILC250 parameters
"set 2": TDR ("baseline 250" from p11 of Yokoya's talk @ AWLC)
"set 4": normalised ex reduced from 10 to 5 mm ("New Param" in Yokoya's table)
"set 15": set 4, but with bx reduced from 13.0 to 9.19 mm
"set 16": set 15, but with by increased from 0.41 to 0.58 mm
Waist shift of 240 mm in x and y
→ Bunches are smaller in the x-direction:
more luminosity
more beamstrahlung
→ larger energy spread of collisions, more detector backgrounds

---
ILC250 parameter sets – Luminosity (CAIN)
From talk by Daniel

---
ILC250 parameter sets – Luminosity (GuineaPig)
Similar at first glance
Lumi_ee histogram values given in main output of GuineaPig
Less information given by GuineaPig
Numbers given in 200 bins
Not detailed enough for peak at 250 GeV
No information for below 1028 cm-2 s-1
Up to 8 * 1033 cm-2 s-1, maybe because of binning

---
ILC250 parameter sets –
Pair Envelopes (CAIN)
3.5 T
ILD
From talk by Daniel

---
ILC250 parameter sets –
Pair Envelopes (CAIN)
From talk by Daniel

---
ILC250 parameter sets –
Pair Envelopes (GuineaPig)
5 T
SiD
Set 1: TDR
Set 4: TDR + ex
Set 15: TDR +
ex + bx
Set 16: TDR +
ex + bx + by

---
ILC250 parameter sets –
Pair Envelopes (GuineaPig)
5 T
SiD
Set 16: TDR +
ex + bx + by
Set 15: TDR +
ex + bx
Set 1: TDR
Set 4: TDR + ex

---
ILC250 parameter sets -
Pair envelopes
Conclusion by Daniel Jeans
In current ILD design with 3.5 T, “beampipe rather close to envelope”
ILD solenoid can reach 4.0 T, but higher field has trade-offs:
reduced low pT track finding efficiency, worse vertex charge measurement
Larger beam pipe, or higher B-field to be considered
Conclusion for SiD
Even in current design, at least “set 4” doesn't seem to be a problem
“Set 15” and “set 16” are more problematic
I will look at the number of hits in the vertex detector layers